Safe Work Practice

TASK: GAS LEAF BLOWER

This task may only be performed by trained and authorized personnel.

| Facility: | Written By: | Approved By: | Date Created: | Date of Last Revision: |
| --- | --- | --- | --- | --- |

| Hazard Present: ejected materials and flying debris (eye injury) noise fire/ hot surfaces allergens (dust and pollen) | Personal Protective Equipment (PPE) or Devices Required: protective eyewear / face shield protective gloves /clothing CSA approved footwear hearing protection dust mask (N95) high visibility vest (if working near traffic or other PME) | Additional Training Requirements: operation manual respirator fit test & training |
| --- | --- | --- |
| NOTE: All practices obtained from mySafetyAssistant™, operator manuals or other samples must have the consultation of workers and be thoroughly reviewed to ensure they are accurate for your workplace and your jobs! Pre-operational safety checks: Inspect leaf blower muffler, air intakes and air filer to ensure they are in good working condition. Ensure that all switches are functioning. Faulty equipment must not be used. Report, or repair suspect machinery immediately to your supervisor. If repairs are necessary, ensure you cut engine, lock-out leaf blower and remove spark plug to avoid injury. PPE Wear CSA footwear to protect feet from tool and flying debris. Always wear long pants and long sleeved shirts to protect from debris. Always wear safety glasses, gloves, dust mask, and hearing protection Operation safety: When starting the leaf blower, point tool towards an open area and hold with two hands. Do not point blower in the direction of people or animals. Ensure bystanders are at least 15 meters away. Stop blowing if you are approached by another person. Ensure you are standing on a stable surface. Never operate blower standing on a ladder, rooftop etc. Use attachments to reach high places. Do not blow towards open windows and doors. When operating, do not allow grass and debris to build up on your tool, as this can lead to damage and breakdown. Never leave blower running unattended. Be aware of the potential for ejected material and ensure that no person or animal is endangered when operating the equipment. Gas Always use caution when working with or around gasoline because it is extremely flammable. Ensure you use the correct fuel mixture in the gas tank. Wrong mixture can damage your tool and could potentially cause injury. Ensure your leaf blower is stored in a secure environment to avoid gas leaks and spills (fire hazard). Fuelling Let engine cool for at least 10 minutes before refueling to avoid risk of ignition. Even if engine is cooled down, always use a proper filling device and exercise caution to prevent spilling onto engine or exhaust. If an emergency occurs while conducting this task, or there is an equipment malfunction, engage emergency stop and follow the lock out procedure. REPORT ANY HAZARDOUS SITUATIONS TO YOUR SUPERVISOR |
| Guidance Documents / Standards/ Applicable Legislation /Other: Guidance Documents: Operator’s Manual CSA Standards CSA Z195.1-02 Protective Footwear CSA Z94.3.1-02 Protective Eyewear CSA Z94.2-02 Hearing Protection Devices Manitoba Workplace Safety and Health Regulation, MR 217/2006 as amended: Part 2.1.1 Safe Work Procedures Part 6.1 Personal Protective Equipment Part 12.3, 12.4 Hearing Protection | This Safe Work Practice will be reviewed any time the task, equipment, or materials change and at a minimum every three years |

This Safe Work Practice has had the consultation of the following workers:

Name_____________________  Signature ____________________   Position  _______________     Date: _________

Name_____________________  Signature ____________________   Position  _______________     Date: _________

Name_____________________  Signature ____________________   Position  _______________     Date: _________