Safe Work Practice

TASK - PROPANE SAFETY

This task may only be performed by trained and authorized personnel.

| Facility: | Written By: | Approved By: | Date Created: | Date of Last Revision: |
| --- | --- | --- | --- | --- |

| Hazard Present: Flammable / explosive Thermal - cold crushing (fallen cylinders) Poison (carbon monoxide) | Personal Protective Equipment (PPE) or Devices Required: protective eyewear / face shield protective gloves CSA approved footwear | Additional Training Requirements: WHMIS Emergency response TDG |
| --- | --- | --- |
| NOTE: All practices obtained from mySafetyAssistant™, operator manuals or other samples must have the consultation of workers and be thoroughly reviewed to ensure they are accurate for your workplace and your jobs! Since propane is heavier than air and invisible, it is a special concern when it is used on the job site. All installations and use of this product on the job site must comply with the Government Legislation set out for its safe use. Suppliers delivering the product or setting up the equipment at the site must be part of the safe work practice. Cylinders must be transported and secured in an upright position in a well ventilated area. Nylon slings must be used in a “choker” fashion when loading, off-loading, or lifting propane tanks. “Lifting lugs” provided on tanks are not to be used. Slings are to be wrapped around the shell of the tank. Tank valves and regulators are to be removed from the tank prior to any movement of the tank. Crane hooks shall be equipped with a “safety latch”. All trucks, cranes or equipment used to handle propane tanks must be equipped with a fire extinguisher appropriate for the size and type of tank being handled. Any movement or repositioning of tanks shall be performed by a competent worker. Tanks are not to be heated to increase flow. When in use, propane bottles are to be securely held in an upright position. Tanks are not to be connected and used without proper regulators. Propane should always be used in a well ventilated area to prevent carbon monoxide poisoning or oxygen depletion. Ensure WHMIS and TDG labels are appropriately attached and visible. Cylinders will not be stored inside buildings, or carried in closed canopies, vehicles or tool vans, following applicable legislation. Cylinders should not be used if shoulder label/stamp is not legible. When not in use, cylinder to be secured in upright position, valve closed and regulator removed If an emergency occurs while conducting this task, or there is an equipment malfunction, engage emergency stop and follow the lock out procedure. REPORT ANY HAZARDOUS SITUATIONS TO YOUR SUPERVISOR |
| Guidance Documents / Standards/ Applicable Legislation /Other: Manitoba Workplace Safety and Health Regulation, MR 217/2006 AS AMENDED: Part 19 Fire and Explosive Hazards Part 35 Workplace Hazardous Materials Information System The Dangerous Goods Handling and Transportation Act | This Safe Work Practice will be reviewed any time the task, equipment, or materials change and at a minimum every three years |

This Safe Work Practice has had the consultation of the following workers:

Name_____________________  Signature ____________________   Position  _______________     Date: _________

Name_____________________  Signature ____________________   Position  _______________     Date: _________

Name_____________________  Signature ____________________   Position  _______________     Date: _________