Safe Work Practice

TASK RIDE ON MOWERS

This task may only be performed by trained and authorized personnel.

| Facility: | Written By: | Approved By: | Date Created: | Date of Last Revision: |
| --- | --- | --- | --- | --- |

| Hazard Present: Flying objects rotating blades Sharp edges Noise Dust and pollen | Personal Protective Equipment (PPE) or Devices Required: Protective eyewear / face shield Protective gloves /clothing CSA approved footwear Hearing protection Dust mask | Additional Training Requirements: Safe equipment operation Respirator fit testing Respirator training |
| --- | --- | --- |
| NOTE: All practices obtained from mySafetyAssistant™, operator manuals or other samples must have the consultation of workers and be thoroughly reviewed to ensure they are accurate for your workplace and your jobs! Pre-operational safety checks: Ensure all safety devices, guards, switches, and shields are fitted, secure and functional. Ensure that seat belt, if fitted, is in sound condition. Ensure cutting blades are secure and in good condition. Ensure that any pneumatic and hydraulic mechanisms are in sound condition. Ensure that all electrical switches (including dead mans switch if fitted) are functioning. Faulty equipment must not be used. Report suspect machinery immediately. Operation safety: Never carry passengers. Be sure the transmission is out of gear and the mower blade clutch disengaged before starting. Keep clear of moving machine parts. Drive at speed slow enough to keep control over unexpected hazards. Travel up/down slopes rather than across taking extra care when ascending/descending steep slopes. Use 150 as the maximum to attempt to mow. Use extreme caution when refueling to prevent spilling fuel onto hot engine or exhaust. Before making adjustments bring the machine to a complete standstill and isolate. Be aware of the potential for ejected material and ensure that no person or animal is endangered when operating the equipment. Stopping and Parking: Park on even ground. Stop the ride on mower and shift the gear selector to park position. Raise and secure the cutting blades. Lock the parking brake. Stop the engine and remove the keys. If an emergency occurs while conducting this task, or there is an equipment malfunction, engage emergency stop and follow the lock out procedure. REPORT ANY HAZARDOUS SITUATIONS TO YOUR SUPERVISOR |
| Guidance Documents / Standards/ Applicable Legislation /Other: Guidance Documents: Operator’s Manual CSA Standards CSA Z195.1-02 Protective Footwear CSA Z94.3.1-02 Protective Eyewear CSA Z94.2-02 Hearing Protection Devices CSA Z94.4-02 Selection, Use, and Care of Respirators Manitoba Workplace Safety and Health Regulation, MR 217/2006 as amended: Part 2.1.1 Safe Work Procedures Part 6.1 Personal Protective Equipment Part 8 Musculoskeletal Injuries Part 12.3, 12.4 Hearing Protection | This Safe Work Practice will be reviewed any time the task, equipment, or materials change and at a minimum every three years |

This Safe Work Practice has had the consultation of the following workers:

Name_____________________  Signature ____________________   Position  _______________     Date: _________

Name_____________________  Signature ____________________   Position  _______________     Date: _________

Name_____________________  Signature ____________________   Position  _______________     Date: _________